## Slide 1: ECE 752 Review: Modern Processors
© Prof. Mikko Lipasti
Lecture notes based in part on slides created by John Shen, Mark Hill, David Wood, Guri Sohi, Jim Smith, Erika Gunadi, Mitch Hayenga, Vignyan Reddy, Dibakar Gope

## Slide 2: High-IPC Processor Evolution
Desktop/Workstation Market
Scalar RISC Pipeline
1980s:
MIPS
SPARC
Intel 486
2-4 Issue
In-order
Early 1990s:
IBM RIOS-I
Intel Pentium
Limited Out-of-Order
Mid 1990s:
PowerPC 604
Intel P6
Large ROB Out-of-Order
2000s:
DEC Alpha 21264
IBM Power4/5
AMD K8
1985 – 2005: 20 years, 100x frequency
Mobile Market
Scalar RISC Pipeline
2002: ARM11
2-4 Issue
In-order
2005: Cortex A8
Limited Out-of-Order
2009: Cortex A9
Large ROB Out-of-Order
2011: Cortex A15
2002 – 2011: 10 years, 10x frequency

## Slide 3: A Typical High-IPC Processor

## Slide 4: Power Consumption
Actual computation overwhelmed by overhead of aggressive execution pipeline
ARM Cortex A15 [Source: NVIDIA]
Core i7 [Source: Intel]

## Slide 5: Mobile CPUs: What Next?
ARM ISA compatibility …
Processor Performance = ---------------
Time
Program
Architecture --> Implementation --> Realization
Compiler Designer Processor Designer Chip Designer
Instructions
Cycles
Program
Instruction
Time
Cycle
(code size)
=
X
X
(CPI)
(cycle time)
NVIDIA Project Denver?
Frequency: maxed out due to power
ILP bag of tricks from desktop CPUs: empty

## Slide 6: ILP is our only option
Attack and reduce overheads one by one
Free up power budget for actual computation
ARM Cortex A15 [Source: NVIDIA]

## Slide 7: Lecture Summary
Motivation
Brief review: High-IPC, out-of-order processors
  Instruction flow
  Register Dataflow
  Memory Dataflow
Caches and Memory Hierarchy

## Slide 8: High-IPC Processor

## Slide 9: Instruction Flow
Challenges:
  Branches: unpredictable
  Branch targets misaligned
  Instruction cache misses
Solutions
  Prediction and speculation
  High-bandwidth fetch logic
  Nonblocking cache and prefetching
Instruction Cache
PC
only3 instructions fetched
Objective: Fetch multiple instructions per cycle
Notes: Don’t starve the pipeline: n/cycle
Must fetch n/cycle from I$

## Slide 10: Disruption of Instruction Flow
Notes: Penalty (increased lost opportunity cost): 1) target addr. Generation, 2) condition resolution
Sketch Tyranny of Amdahl’s Law pipeline diagram

## Slide 11: Branch Prediction
Target address generation  Target Speculation
  Access register:
    PC, General purpose register, Link register
  Perform calculation:
    +/- offset, autoincrement
Condition resolution  Condition speculation
  Access register:
    Condition code register, General purpose register
  Perform calculation:
    Comparison of data register(s)
Notes: Non-CC architecture requires actual computation to resolve condition

## Slide 12: Target Address Generation
Notes: Decode: PC = PC + DISP (adder) (1 cycle penalty)
Dispatch: PC = (R2) ( 2 cycle penalty)
Execute: PC = (R2) + offset (3 cycle penalty)
Both cond & uncond
Guess target address? Keep history based on branch address

## Slide 13: Branch Condition Resolution
Notes: Dispatch: RD (2 cycle penalty)
Execute: Status (3 cycle penalty)
Both cond & uncond
Guess taken vs. not taken

## Slide 14: Branch Instruction Speculation
Notes: Fetch: PC = PC + 4
BTB (cache) contains k cycles of history, generates guess
Execute: corrects wrong guess

## Slide 15: Hardware Smith Predictor
Jim E. Smith. A Study of Branch Prediction Strategies. International Symposium on Computer Architecture, pages 135-148, May 1981
Widely employed: Intel Pentium, PowerPC 604, MIPS R10000, etc.

## Slide 16: Cortex A15: Bi-Mode Predictor
PHT partitioned into T/NT halves
  Selector chooses source
Reduces negative interference, since most entries in PHT0 tend towards NT, and most entries in PHT1 tend towards T
15% of A15 Core Power!

## Slide 17: Branch Target Prediction
Does not work well for function/procedure returns
Does not work well for virtual functions, switch statements

## Slide 18: Branch Speculation
Leading Speculation
  Done during the Fetch stage
  Based on potential branch instruction(s) in the current fetch group
Trailing Confirmation
  Done during the Branch Execute stage
  Based on the next Branch instruction to finish execution

## Slide 19: Branch Speculation
Start new correct path
  Must remember the alternate (non-predicted) path
Eliminate incorrect path
  Must ensure that the mis-speculated instructions produce no side effects
Notes: “squash” on instructions following NT prediction

## Slide 20: Mis-speculation Recovery
Start new correct path
  Update PC with computed branch target (if predicted NT)
  Update PC with sequential instruction address (if predicted T)
  Can begin speculation again at next branch
Eliminate incorrect path
  Use tag(s) to deallocate resources occupied by speculative instructions
  Invalidate all instructions in the decode and dispatch buffers, as well as those in reservation stations

## Slide 21: Parallel Decode
Primary Tasks
  Identify individual instructions (!)
  Determine instruction types
  Determine dependences between instructions
Two important factors
  Instruction set architecture
  Pipeline width
Notes: RISC vs. CISC: inherently serial
Find branches early: redirect fetch
Detect dependences: nxn comparators (pairwise)
RISC: fixed length, regular format, easier
CISC: can be multiple stages (lots of work), P6: I$ => decode is 5 cycles, often translates into internal RISC-like uops or ROPs

## Slide 22: Pentium Pro Fetch/Decode
Notes: 16B/cycle delivered from I$ into FIFO instruction buffer
Decoder 0 is fully general, 1 & 2 can handle only simple uops.
Enter centralized window (reservation station); wait here until operands ready, structural hazards resolved.
Why is this bad? Branch penalty; need a good branch predictor.
Other option: predecode bits

## Slide 23: Dependence Checking
Trailing instructions in fetch group
  Check for dependence on leading instructions
Dest
Src0
Src1
Dest
Src0
Src1
Dest
Src0
Src1
Dest
Src0
Src1
?=
?=
?=
?=
?=
?=
?=
?=
?=
?=
?=
?=

## Slide 24: Summary: Instruction Flow
Fetch group alignment
Target address generation
  Branch target buffer
Branch condition prediction
Speculative execution
  Tagging/tracking instructions
  Recovering from mispredicted branches
Decoding in parallel

## Slide 25: High-IPC Processor

## Slide 26: Register Data Flow
Parallel pipelines
  Centralized instruction fetch
  Centralized instruction decode
Diversified execution pipelines
  Distributed instruction execution
Data dependence linking
  Register renaming to resolve true/false dependences
  Issue logic to support out-of-order issue
  Reorder buffer to maintain precise state

## Slide 27: Issue Queues and Execution Lanes
Source: theregister.co.uk
ARM Cortex A15
Notes: Distributed, with localized control (easy win: break up based on data type, I.e. FP vs. integer)
Less efficient utilization, but each unit is smaller since can be single-ported (for dispatch and issue)
Must tune for proper utilization

## Slide 28: Program Data Dependences
True dependence (RAW)
  j cannot execute until i produces its result
Anti-dependence (WAR)
  j cannot write its result until i has read its sources
Output dependence (WAW)
  j cannot write its result until i has written its result

## Slide 29: Register Data Dependences
Program data dependences cause hazards
  True dependences (RAW)
  Antidependences (WAR)
  Output dependences (WAW)
When are registers read and written?
  Out of program order!
  Hence, any and all of these can occur
Solution to all three: register renaming

## Slide 30: Register Renaming: WAR/WAW
Widely employed (Core i7, Cortex A15, …)
Resolving WAR/WAW:
  Each register write gets unique “rename register”
  Writes are committed in program order at Writeback
  WAR and WAW are not an issue
    All updates to “architected state” delayed till writeback
    Writeback stage always later than read stage
  Reorder Buffer (ROB) enforces in-order writeback
Add R3 <= … P32 <= …
Sub R4 <= … P33 <= …
And R3 <= … P35 <= …

## Slide 31: Register Renaming: RAW
In order, at dispatch:
  Source registers checked to see if “in flight”
    Register map table keeps track of this
    If not in flight, can be read from the register file
    If in flight, look up “rename register” tag (IOU)
  Then, allocate new register for register write
Add R3 <= R2 + R1 P32 <= P2 + P1
Sub R4 <= R3 + R1 P33 <= P32 + P1
And R3 <= R4 & R2 P35 <= P33 + P2

## Slide 32: Register Renaming: RAW
Advance instruction to instruction queue
  Wait for rename register tag to trigger issue
Issue queue/reservation station enables out-of-order issue
  Newer instructions can bypass stalled instructions
Source: theregister.co.uk

## Slide 33: High-IPC Processor

## Slide 34: Memory Data Flow
Resolve WAR/WAW/RAW memory dependences
  MEM stage can occur out of order
Provide high bandwidth to memory hierarchy
  Non-blocking caches

## Slide 35: Memory Data Dependences
WAR/WAW: stores commit in order
  Hazards not possible.
RAW: loads must check pending stores
  Store queue keeps track of pending stores
  Loads check against these addresses
  Similar to register bypass logic
  Comparators are 64 bits wide
  Must consider position (age) of loads and stores
Major source of complexity in modern designs
  Store queue lookup is position-based
  What if store address is not yet known?
Store
Queue
Load/Store RS
Agen
Reorder Buffer
Mem

## Slide 36: Increasing Memory Bandwidth
Expensive to duplicate
Complex, concurrent FSMs
Notes: Duplicating load/store pipelines is fundamentally harder because they contain shared state (in the cache)
Loads that miss can be set aside in a “missed load buffer” or “miss status handling register” (MSHR)
Subsequent loads that hit can still be handled

## Slide 37: Maintaining Precise State
Out-of-order execution
  ALU instructions
  Load/store instructions
In-order completion/retirement
  Precise exceptions
Solutions
  Reorder buffer retires instructions in order
  Store queue retires stores in order
  Exceptions can be handled at any instruction boundary by reconstructing state out of ROB/SQ
ROB
Head
Tail
Notes: Precise exception – clean instr. Boundary for restart
Memory consistency – WAW, also subtle multiprocessor issues (in 757)
Memory coherence – RAR expect later load to also see new value seen by earlier load

## Slide 38: Summary: A High-IPC Processor

## Slide 39: Memory Hierarchy
Registers
On-Chip
SRAM
Off-Chip
SRAM
DRAM
Disk
CAPACITY
SPEED and COST

## Slide 40: Why Memory Hierarchy?
Need lots of bandwidth
Need lots of storage
  64MB (minimum) to multiple TB
Must be cheap per bit
  (TB x anything) is a lot of money!
These requirements seem incompatible

## Slide 41: Why Memory Hierarchy?
Fast and small memories
  Enable quick access (fast cycle time)
  Enable lots of bandwidth (1+ L/S/I-fetch/cycle)
Slower larger memories
  Capture larger share of memory
  Still relatively fast
Slow huge memories
  Hold rarely-needed state
  Needed for correctness
All together: provide appearance of large, fast memory with cost of cheap, slow memory

## Slide 42: Why Does a Hierarchy Work?
Locality of reference
  Temporal locality
    Reference same memory location repeatedly
  Spatial locality
    Reference near neighbors around the same time
Empirically observed
  Significant!
  Even small local storage (8KB) often satisfies >90% of references to multi-MB data set

## Slide 43: Memory Hierarchy
CPU
I & D L1 Cache
Shared L2 Cache
Main Memory
Disk
Temporal Locality
Keep recently referenced items at higher levels
Future references satisfied quickly
Spatial Locality
Bring neighbors of recently referenced to higher levels
Future references satisfied quickly

## Slide 44: Four Burning Questions
These are:
  Placement
    Where can a block of memory go?
  Identification
    How do I find a block of memory?
  Replacement
    How do I make space for new blocks?
  Write Policy
    How do I propagate changes?
Consider these for caches
  Built from SRAM, EDRAM, stacked DRAM

## Slide 45: Placement
Memory Type | Placement | Comments
Registers | Anywhere; Int, FP, SPR | Compiler/programmer manages
Cache (SRAM) | Fixed in H/W | Direct-mapped, set-associative, fully-associative
DRAM | Anywhere | O/S manages
Disk | Anywhere | O/S manages
HUH?

## Slide 46: Placement
Address Range
  Exceeds cache capacity
Map address to finite capacity
  Called a hash
  Usually just masks high-order bits
Direct-mapped
  Block can only exist in one location
  Hash collisions cause problems
SRAM Cache
Hash
Address
Index
Data Out
Index
Offset
32-bit Address
Offset
Block Size

## Slide 47: Placement
Fully-associative
  Block can exist anywhere
  No more hash collisions
Identification
  How do I know I have the right block?
  Called a tag check
    Must store address tags
    Compare against address
Expensive!
  Tag & comparator per block
SRAM Cache
Hash
Address
Data Out
Offset
32-bit Address
Offset
Tag
Hit
Tag Check
?=
Tag

## Slide 48: Placement
Set-associative
  Block can be in a locations
  Hash collisions:
    a still OK
Identification
  Still perform tag check
  However, only a in parallel
SRAM Cache
Hash
Address
Data Out
Offset
Index
Offset
32-bit Address
Tag
Index
a Tags
a Data Blocks
Index
?=
?=
?=
?=
Tag

## Slide 49: Placement and Identification
Consider: <BS=block size, S=sets, B=blocks>
  <64,64,64>: o=6, i=6, t=20: direct-mapped (S=B)
  <64,16,64>: o=6, i=4, t=22: 4-way S-A (S = B / 4)
  <64,1,64>: o=6, i=0, t=26: fully associative (S=1)
Total size = BS x B = BS x S x (B/S)
Offset
32-bit Address
Tag
Index
Portion | Length | Purpose
Offset | o=log2(block size) | Select word within block
Index | i=log2(number of sets) | Select set of blocks
Tag | t=32 - o - i | ID block within set

## Slide 50: Replacement
Cache has finite size
  What do we do when it is full?
Analogy: desktop full?
  Move books to bookshelf to make room
Same idea:
  Move blocks to next level of cache

## Slide 51: Replacement
How do we choose victim?
  Verbs: Victimize, evict, replace, cast out
Several policies are possible
  FIFO (first-in-first-out)
  LRU (least recently used)
  NMRU (not most recently used)
  Pseudo-random (yes, really!)
Pick victim within set where a = associativity
  If a <= 2, LRU is cheap and easy (1 bit)
  If a > 2, it gets harder
  Pseudo-random works pretty well for caches

## Slide 52: Write Policy
Memory hierarchy
  2 or more copies of same block
    Main memory and/or disk
    Caches
What to do on a write?
  Eventually, all copies must be changed
  Write must propagate to all levels
    And other processor’s caches (later)

## Slide 53: Write Policy
Easiest policy: write-through
Every write propagates directly through hierarchy
  Write in L1, L2, memory, disk (?!?)
Why is this a bad idea?
  Very high bandwidth requirement
  Remember, large memories are slow
Popular in real systems only to the L2
  Every write updates L1 and L2
  Beyond L2, use write-back policy

## Slide 54: Write Policy
Most widely used: write-back
Maintain state of each line in a cache
  Invalid – not present in the cache
  Clean – present, but not written (unmodified)
  Dirty – present and written (modified)
Store state in tag array, next to address tag
  Mark dirty bit on a write
On eviction, check dirty bit
  If set, write back dirty line to next level
  Called a writeback or castout

## Slide 55: Write Policy
Complications of write-back policy
  Stale copies lower in the hierarchy
  Must always check higher level for dirty copies before accessing copy in a lower level
Not a big problem in uniprocessors
  In multiprocessors: the cache coherence problem
I/O devices that use DMA (direct memory access) can cause problems even in uniprocessors
  Called coherent I/O
  Must check caches for dirty copies before reading main memory

## Slide 56: Cache Example
Tag0 | Tag1 | LRU
 |  | 0
 |  | 0
 |  | 0
 |  | 0
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Tag Array

## Slide 57: Cache Example
Tag0 | Tag1 | LRU
 |  | 0
 |  | 0
10 |  | 1
 |  | 0
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Tag Array

## Slide 58: Cache Example
Tag0 | Tag1 | LRU
 |  | 0
 |  | 0
10 |  | 1
 |  | 0
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Tag Array

## Slide 59: Cache Example
Tag0 | Tag1 | LRU
 |  | 0
 |  | 0
10 |  | 1
11 |  | 1
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Load 0x3C | 111100 | 3/0 | Miss
Tag Array

## Slide 60: Cache Example
Tag0 | Tag1 | LRU
10 |  | 1
 |  | 0
10 |  | 1
11 |  | 1
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Load 0x3C | 111100 | 3/0 | Miss
Load 0x20 | 100000 | 0/0 | Miss
Tag Array

## Slide 61: Cache Example
Tag0 | Tag1 | LRU
10 | 11 | 0
 |  | 0
10 |  | 1
11 |  | 1
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Load 0x3C | 111100 | 3/0 | Miss
Load 0x20 | 100000 | 0/0 | Miss
Load 0x33 | 110011 | 0/1 | Miss
Tag Array

## Slide 62: Cache Example
Tag0 | Tag1 | LRU
01 | 11 | 1
 |  | 0
10 |  | 1
11 |  | 1
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Load 0x3C | 111100 | 3/0 | Miss
Load 0x20 | 100000 | 0/0 | Miss
Load 0x33 | 110011 | 0/1 | Miss
Load 0x11 | 010001 | 0/0 (lru) | Miss/Evict
Tag Array

## Slide 63: Cache Example
Tag0 | Tag1 | LRU
01 | 11 | 1
 |  | 0
10 d |  | 1
11 |  | 1
32B Cache: <BS=4,S=4,B=8>
  o=2, i=2, t=2; 2-way set-associative
  Initially empty
  Only tag array shown on right
Trace execution of:
Reference | Binary | Set/Way | Hit/Miss
Load 0x2A | 101010 | 2/0 | Miss
Load 0x2B | 101011 | 2/0 | Hit
Load 0x3C | 111100 | 3/0 | Miss
Load 0x20 | 100000 | 0/0 | Miss
Load 0x33 | 110011 | 0/1 | Miss
Load 0x11 | 010001 | 0/0 (lru) | Miss/Evict
Store 0x29 | 101001 | 2/0 | Hit/Dirty
Tag Array

## Slide 64: Cache Misses and Performance
Miss penalty
  Detect miss: 1 or more cycles
  Find victim (replace block): 1 or more cycles
    Write back if dirty
  Request block from next level: several cycles
    May need to find line from one of many caches (coherence)
  Transfer block from next level: several cycles
    (block size) / (bus width)
  Fill block into data array, update tag array: 1+ cycles
  Resume execution
In practice: 6 cycles to 100s of cycles

## Slide 65: Cache Miss Rate
Determined by:
  Program characteristics
    Temporal locality
    Spatial locality
  Cache organization
    Block size, associativity, number of sets

## Slide 66: Cache Miss Rates: 3 C’s [Hill]
Compulsory miss
  First-ever reference to a given block of memory
  Cold misses = mc : number of misses for FA infinite cache
Capacity
  Working set exceeds cache capacity
  Useful blocks (with future references) displaced
  Capacity misses = mf - mc : add’l misses for finite FA cache
Conflict
  Placement restrictions (not fully-associative) cause useful blocks to be displaced
  Think of as capacity within set
  Conflict misses = ma - mf : add’l misses in actual cache
Notes: Model 3 caches: FA/infinite with mc misses, FA/finite with mf misses, actual with ma misses

## Slide 67: Cache Miss Rate Effects
Number of blocks (sets x associativity)
  Bigger is better: fewer conflicts, greater capacity
Associativity
  Higher associativity reduces conflicts
  Very little benefit beyond 8-way set-associative
Block size
  Larger blocks exploit spatial locality
  Usually: miss rates improve until 64B-256B
  512B or more miss rates get worse
    Larger blocks less efficient: more capacity misses
    Fewer placement choices: more conflict misses

## Slide 68: Cache Miss Rate
Subtle tradeoffs between cache organization parameters
  Large blocks reduce compulsory misses but increase miss penalty
    #compulsory ~= (working set) / (block size)
    #transfers = (block size)/(bus width)
  Large blocks increase conflict misses
    #blocks = (cache size) / (block size)
  Associativity reduces conflict misses
  Associativity increases access time
Can associative cache ever have higher miss rate than direct-mapped cache of same size?
Notes: Given: A, B, C, A, B, C where A&B conflict but C doesn’t, a DM cache will miss on A & B but hit on C (33% hit rate), whereas a FA cache will always miss

## Slide 69: Cache Miss Rates: 3 C’s
Vary size and associativity
  Compulsory misses are constant
  Capacity and conflict misses are reduced

## Slide 70: Cache Miss Rates: 3 C’s
Vary size and block size
  Compulsory misses drop with increased block size
  Capacity and conflict can increase with larger blocks

## Slide 71: Multilevel Caches
Ubiquitous in high-performance processors
  Gap between L1 (core frequency) and main memory too high
  Level 2 usually on chip, level 3 on or off-chip, level 4 off chip
Inclusion in multilevel caches
  Multi-level inclusion holds if L2 cache is superset of L1
  Can handle virtual address synonyms
  Filter coherence traffic: if L2 misses, L1 needn’t see snoop
  Makes L1 writes simpler
    For both write-through and write-back

## Slide 72: Multilevel Inclusion
Example: local LRU not sufficient to guarantee inclusion
  Assume L1 holds two and L2 holds three blocks
  Both use local LRU
Final state: L1 contains 1, L2 does not
  Inclusion not maintained
Different block sizes also complicate inclusion
P
1
4
2
3
4
1,2,1,3,1,4
1,2,3,4

## Slide 73: Multilevel Inclusion
Inclusion takes effort to maintain
  Make L2 cache have bits or pointers giving L1 contents
  Invalidate from L1 before replacing from L2
  In example, removing 1 from L2 also removes it from L1
Number of pointers per L2 block
  L2 blocksize/L1 blocksize
Supplemental reading: [Wang, Baer, Levy ISCA 1989]
P
1
4
2
3
4
1,2,1,3,1,4
1,2,3,4

## Slide 74: Multilevel Miss Rates
Miss rates of lower level caches
  Affected by upper level filtering effect
  LRU becomes LRM, since “use” is “miss”
  Can affect miss rates, though usually not important
Miss rates reported as:
  Miss per instruction
  Global miss rate
  Local miss rate
  “Solo” miss rate
    L2 cache sees all references (unfiltered by L1)

## Slide 75: Cache Design: Four Key Issues
These are:
  Placement
    Where can a block of memory go?
  Identification
    How do I find a block of memory?
  Replacement
    How do I make space for new blocks?
  Write Policy
    How do I propagate changes?
Consider these for caches
  Usually SRAM
Also apply to main memory, disks

## Slide 76: Replacement
Cache has finite size
  What do we do when it is full?
Analogy: desktop full?
  Move books to bookshelf to make room
  Bookshelf full? Move least-used to library
  Etc.
Same idea:
  Move blocks to next level of cache

## Slide 77: Replacement
How do we choose victim?
  Verbs: Victimize, evict, replace, cast out
Many policies are possible
  FIFO (first-in-first-out)
  LRU (least recently used), pseudo-LRU
  LFU (least frequently used)
  NMRU (not most recently used)
  NRU
  Pseudo-random (yes, really!)
  Optimal
  Etc

## Slide 78: Optimal Replacement Policy?
[Belady, IBM Systems Journal, 1966]
Evict block with longest reuse distance
  i.e. next reference to block is farthest in future
  Requires knowledge of the future!
Can’t build it, but can model it with trace
  Process trace in reverse
  [Sugumar&Abraham] describe how to do this in one pass over the trace with some lookahead (Cheetah simulator)
Useful, since it reveals opportunity
  (X,A,B,C,D,X): LRU 4-way SA $, 2nd X will miss

## Slide 79: Least-Recently Used
For a=2, LRU is equivalent to NMRU
  Single bit per set indicates LRU/MRU
  Set/clear on each access
For a>2, LRU is difficult/expensive
  Timestamps? How many bits?
    Must find min timestamp on each eviction
  Sorted list? Re-sort on every access?
List overhead: log2(a) bits /block
  Shift register implementation

## Slide 80: True LRU Shortcomings
Streaming data/scans: x0, x1, …, xn
  Effectively no temporal reuse
Thrashing: reuse distance > a
  Temporal reuse exists but LRU fails
All blocks march from MRU to LRU
  Other conflicting blocks are pushed out
For n>a no blocks remain after scan/thrash
  Incur many conflict misses after scan ends
Pseudo-LRU sometimes helps a little bit

## Slide 81: Segmented or Protected LRU
[I/O: Karedla, Love, Wherry, IEEE Computer 27(3), 1994]
[Cache: Wilkerson, Wade, US Patent 6393525, 1999]
Partition LRU list into filter and reuse lists
On insert, block goes into filter list
On reuse (hit), block promoted into reuse list
Provides scan & some thrash resistance
  Blocks without reuse get evicted quickly
  Blocks with reuse are protected from scan/thrash blocks
No storage overhead, but LRU update slightly more complicated

## Slide 82: Protected LRU: LIP
Simplified variant of this idea: LIP
  Qureshi et al. ISCA 2007
Insert new blocks into LRU position, not MRU position
  Filter list of size 1, reuse list of size (a-1)
Do this adaptively: DIP
Use set dueling to decide LIP vs. LRU
  1 (or a few) set uses LIP vs. 1 that uses LRU
  Compare hit rate for sets
  Set policy for all other sets to match best set

## Slide 83: Not Recently Used (NRU)
Keep NRU state in 1 bit/block
  Bit is set to 0 when installed (assume reuse)
  Bit is set to 0 when referenced (reuse observed)
  Evictions favor NRU=1 blocks
  If all blocks are NRU=0
    Eviction forces all blocks in set to NRU=1
    Picks one as victim (can be pseudo-random, or rotating, or fixed left-to-right)
Simple, similar to virtual memory clock algorithm
Provides some scan and thrash resistance
  Relies on “randomizing” evictions rather than strict LRU order
Used by Intel Itanium, Sparc T2

## Slide 84: Least Frequently Used
Counter per block, incremented on reference
Evictions choose lowest count
  Logic not trivial (a2 comparison/sort)
Storage overhead
  1 bit per block: same as NRU
  How many bits are helpful?

## Slide 85: Pitfall: Cache Filtering Effect
Upper level caches (L1, L2) hide reference stream from lower level caches
Blocks with “no reuse” @ LLC could be very hot (never evicted from L1/L2)
Evicting from LLC often causes L1/L2 eviction (due to inclusion)
Could hurt performance even if LLC miss rate improves

## Slide 86: Replacement Policy Summary
Replacement policies affect capacity and conflict misses
Policies covered:
  Belady’s optimal replacement
  Least-recently used (LRU)
  Practical pseudo-LRU (tree LRU)
  Protected LRU
    LIP/DIP variant
    Set dueling to dynamically select policy
  Not-recently-used (NRU) or clock algorithm
  Least frequently used (LFU)

## Slide 87: Main Memory
DRAM chips
Memory organization
  Interleaving
  Banking
Memory controller design

## Slide 88: DRAM Chip Organization
Optimized for density, not speed
Data stored as charge in capacitor
Discharge on reads => destructive reads
Charge leaks over time
  refresh every 64ms
Cycle time roughly twice access time
Need to precharge bitlines before access

## Slide 89: DRAM Chip Organization
Current generation DRAM
  8Gbit @25nm
  266 MHz synchronous interface
  Data clock 4x (1066MHz), double-data rate so 2133 MT/s
Address pins are time-multiplexed
  Row address strobe (RAS)
  Column address strobe (CAS)

## Slide 90: DRAM Chip Organization
New RAS results in:
  Bitline precharge
  Row decode, sense
  Row buffer write (up to 8K)
New CAS
  Read from row buffer
  Much faster (3x)
Streaming row accesses desirable

## Slide 91: Memory Controller Organization
ReadQ
WriteQ
RespQ
Scheduler
Buffer
DIMM(s)
DIMM(s)
Bank0
Bank1
Commands
Data
Commands
Data
Memory
Controller

## Slide 92: Memory Controller Organization
ReadQ
  Buffers multiple reads, enables scheduling optimizations
WriteQ
  Buffers writes, allows reads to bypass writes, enables scheduling opt.
RespQ
  Buffers responses until bus available
Scheduler
  FIFO? Or schedule to maximize for row hits (CAS accesses)
  Scan queues for references to same page
  Looks similar to issue queue with page number broadcasts for tag match
Buffer
  Builds transfer packet from multiple memory words to send over processor bus

## Slide 93: Lecture Summary
Brief review: High-IPC, out-of-order processors
  Instruction flow
  Register Dataflow
  Memory Dataflow
Caches and Memory Hierarchy
Main memory (DRAM)