## Slide 1: Short Circuiting Memory Traffic in Handheld Platforms
Paper presented in MICRO 2014
Review by Ajay Sekar
*Graphs and figures used from paper “Short Circuiting memory traffic in Handheld platforms”

## Slide 2: Problem Statement
Many media IP’s being integrated in the SoC.
Applications related to media and graphics generate a lot of memory traffic
LPDDR3 Memory throughput - 5.3 GB/s 1 CH , 1333 MHz.
Memory Controller turns out to be the bottleneck …
  http://blog.imgtec.com/multimedia/the-day-i-designed-my-own-mobile-soc

## Slide 3: Usage
Application Characteristics
1.Real time responsiveness - to maintain quality.
2. Frame transactions contain MB’s of data transfer.
3. Data has to be transferred with multiple IP’s
This could overwhelm the memory system

## Slide 4
Frames from multiple IP’s can stress the memory .
Consequences
  IP’s stall for the memory requests
  Energy Wastage… IP’s powered on for a longer time
  Core requests have to contend with high IP memory traffic.

## Slide 5: High Level Solutions
Optimize memory transactions between IP’s in a flow
Decongest System Agent.
Improve memory latency

## Slide 6: Defining a Flow …
(1) Device driver issues a request to the IP with physical address location
(2) IP sends data read requests … gets queued up and prioritized… response received
(3) Complete frame is written back to the memory
(4) Core invokes IP2
(5) IP2 reads data written by IP1

## Slide 7: Memory stalls - Analysis
IP that spend more time on compute = Less stalls
Camera and Graphics App send huge frames of data … leading to stalls
Stalls leads to frame drops
Demand way higher than supply

## Slide 8
4x IP’s have more stalls
Improving Mem Freq does not help
Problem : Queuing latency in the Mem Controller

## Slide 9: Performance Optimization
Yes !!
Reuse distances vary with respect to the application.
Large frames - 10 ms reuse distance
Small frames - <1 ms reuse distance
Can locality be used to exploit the distance … coming up next
Is there reuse of data between IP’s ?

## Slide 10: SOL 1 : Can caches help in data reuse between IP’s ?
Idea - Have a shared cache between the memory and the IP which can be used by all IP’s
Observation - Avg Hit Rates Vs the Cache sizes
A2, A3 - Have small frames - fit inside 4 MB cache
A1,A4,A5 benefit from increasing the cache size , better hit rates
A8 doesn't show any improvement -
      - Frame size too large to fit into a 32 MB cache
      - Reuse distance is large - data would get evicted by frames in the flow or by other flows in the system

## Slide 11
Observation - Average cycles consumes by the IP’s
SND - small frames , larger caches would mean longer lookups
DC - frames fit into larger caches(32 MB), better performance
AE is latency tolerant - more computation - thus cache size does not affect performance
Conclusions
Bigger caches affect area and power budgets.
Large IP-IP reuse distance - main cause of the memory stalls.

## Slide 12
Goal - To reduce IP-IP reuse distance
Similar to “tiling” concept used in matrix multiplication.
  SOL 2 : Sub-Framing
Blocked Matrix Multiply
http://www.eecs.harvard.edu/~mdw/course/cs61/mediawiki/images/b/bb/Lectures-cacheperf.pdf

## Slide 13
Frames are divided into sub-frames
IP’s process data in sub-frame granularity - IP2 would be be invoked if IP1 had completed a sub-frame
Observation : Sub frame Size Vs reuse distance
re-use distance exponentially decreases with decrease in sub-frame size.
Flow buffers and IP-IP short circuiting utilize the sub-framing concept.
  Sub-Framing (contd)

## Slide 14
Private buffers which are place between IP’s
Buffers reuse the data and prevent consume IP from accessing the memory.
- Flow buffers require extra hardware
  Flow Buffers
  IP A
  IP B
IP C
read subframe from memory
write subframe to memory
Reduces intermediate memory accesses

## Slide 15
Similar to “store-load forwarding”
Forward the the stores of IP1 in memory queues to loads of IP2
Works only if the sub-frame reuse distance is small.
  IP-IP Short-circuiting

## Slide 16
OS and HW Support
SA-HAL layer is added - maintains the flow information
SA holds matrix of consumer and producer IP’s in a flow.
SA-HAL logs the producer and consumer of a flow in the flow.
Consumer is informed when the sub-frame is completed.
Implementation

## Slide 17: Effect of sub framing with Flow buffering and Short circuiting
Youtube has better hit rates with Flow buffer and IP-IP short circuiting.
Hit rates increase with increase in buffer sizes
Memory bottleneck is reduced …

## Slide 18
% of frames completed with baseline, subframe-cache and subframe-fwd
Performance Gains
Application that benefit SB-C and SB-F see 45 % reduction in cycles per frame
VD-DC , loss of 17 % - parallel working IP’s stress the memory

## Slide 19
Energy Gains
Avg 40% reduction in active cycles
Memory energy consumption is reduced by 33%
      Reduced DRAM accesses

## Slide 20
    Conclusion
Optimized System Agent to reduce memory traffic
Exploring locality to reuse the data. - reducing memory accesses.
Avg 45 % performance gains for media/graphics application (exceptions)
Energy consumption of IP’s and memory reduced.

## Slide 21: Backup Slides

## Slide 22: Flows

## Slide 23: Platform Configuration

## Slide 24: System Agent
  Application makes API calls to invoke the HW
Device Drivers transforms API calls in IP invocations
Control signal given to the IP - registers and memory pointers
IP’s reads and write values into the Memory using DMA