## Slide 1: Coherence Protocol for Transparent Management of Scratchpad Memories in Shared Memory Manycore Architectures
Lluc Álvarez, Lluís Vilanova, Miquel Moretó,
Marc Casas, Marc Gonzàlez, Xavier Martorell,
Nacho Navarro, Eduard Ayguadé, Mateo Valero
Discussion Lead By: Vijay Thiruvengadam

## Slide 2: Introduction
Traditional Hardware Caching a problem in future manycores
Hybrid memory hierarchies in HPC (like GPU)
  Power efficiency
  Scalability
  Programmability
  Caches
    Power efficiency
    Scalability
    Programmability
  Scratchpad memories
    Power efficiency
    Scalability
    Programmability
Notes: Scratchpad memory reply on the SW identifying the private data and redirect it to the SPM. This eliminates coherence traffic for this private data and reduce the number of cache misses

## Slide 3: Introduction
Our goal
  Introduce SPMs alongside the L1 cache
    Advantages in power and scalability
  Combination of compiler, runtime and hardware techniques manage the SPMs and coherence between SPM & regular memory
    Minimal programmer involvement
Overview of Solution
  Compiler transforms code based on programmer annotation and compiler analysis
  Memory accesses split into – regular (GM) access, scratchpad (SPM) access, potentially aliased (Guarded GM) access
  Hardware intercepts guarded accesses and redirects them to SPM in case it is aliased with SPM data
C
C
L1
Cluster Interconnect
SPM
L1
SPM
C
C
L1
SPM
L1
SPM
C
C
L1
SPM
L1
SPM
C
C
L1
SPM
L1
SPM
DRAM
DRAM
L2

## Slide 4: Hybrid Memory Hierarchy
Code Transformation
  Programmer annotates code suitable for transformation
  Compiler applies tiling transformations
    Strided accesses mapped to the SPM
    Random accesses mapped to the cache hierarchy
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
Strided: a, b
Random: c, ptr
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
i=0;
while (i<N)
{
MAP (&a[i], _a, iters, tags);
MAP (&b[i], _b, iters, tags);
n = (i+iters>N) ? N : i+iters;
SYNCH (tags)
for (_i=0; _i<n; _i++, i++)
{
_a[_i] = _b[_i];
c[_b[_i]] = 0;
ptr[_a[_i]]++;
}
}
Control
Work
Synch
C
L1
SPM
a, b
c, ptr

## Slide 5: Coherence Problem
SPMs are not coherent with the cache hierarchy
  Invalid results if strided and random accesses alias
Very challenging problem for the compiler
  Alias analysis
Restrictive or inefficient solutions
  Programmer identifies private data and applies code transformations
  Prior work by authors proposes similar solution but restricts a core to access only it’s own SPM
Our solution solves this issue
  Compiler can generate code and mark accesses that might be aliased
  Hardware intercepts these potentially aliased accesses and resolves it

## Slide 6: Outline
Introduction
  Hybrid memory hierarchy
  Coherence problem
Hardware-software coherence protocol
  Compiler support
  Hardware design
Evaluation
  Experimental framework
  Comparison with cache hierarchies
Conclusions

## Slide 7: Hardware-Software Coherence Protocol
Basic idea
  Avoid maintaining two coherent copies of the data
  Ensure the valid copy is always accessed
Compiler detects potentially incoherent accesses
  Emits guarded memory instructions
Hardware diverts them to the valid copy of the data
  Distributed hardware directory to track the contents of the SPMs
  Hierarchy of filters to track data not mapped to any SPM on any core

## Slide 8: Compiler Support
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
Step 1: Classification of memory references
  Strided accesses
  Random accesses
  Potentially incoherent accesses
Strided: a, b
Random: c
Potentially incoherent: ptr
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
C
Dir
ptr
L1
SPM
a, b
c

## Slide 9: Compiler Support
Step 2: Code transformation
  Only for strided accesses
    Apply tiling
    Change memory references
for (i=0; i<N; i++)
{
a[i] = b[i];
c[b[i]] = 0;
ptr[a[i]]++;
}
i=0;
while (i<N)
{
MAP (&a[i], _a, iters, tags);
MAP (&b[i], _b, iters, tags);
n = (i+iters>N) ? N : i+iters;
SYNCH (tags)
for (_i=0; _i<n; _i++, i++)
{
_a[_i] = _b[_i];
c[_b[_i]] = 0;
ptr[_a[_i]]++;
}
}
Control
Work
Synch

## Slide 10: Compiler Support
Step 3: Code generation
  Guarded memory instructions for potentially incoherent accesses
i=0;
while (i<N)
{
MAP (&a[i], _a, iters, tags);
MAP (&b[i], _b, iters, tags);
n = (i+iters>N) ? N : i+iters;
SYNCH (tags)
for (_i=0; _i<n; _i++, i++)
{
// _a[_i] = _b[_i];
ld _b(,_i,4),r1
st r1,_a(,_i,4)
// c[_b[_i]] = 0;
mv #0,r3
st r3,c(,r1,4)
// ptr[_a[_i]]++;
gld ptr(,r1,4),r2
inc r2,r2
gst r2,ptr(,r1,4)
}
}
Control
Work
Synch
i=0;
while (i<N)
{
MAP (&a[i], _a, iters, tags);
MAP (&b[i], _b, iters, tags);
n = (i+iters>N) ? N : i+iters;
SYNCH (tags)
for (_i=0; _i<n; _i++, i++)
{
_a[_i] = _b[_i];
c[_b[_i]] = 0;
ptr[_a[_i]]++;
}
}
Control
Work
Synch

## Slide 11: Hardware Design
Distributed hardware directory (SPMDir)
  One directory CAM per core
  Each core tracks contents of its SPM
  Maps regular address to SPM address
Filter
  One filter CAM per core
  Track data not mapped to any SPM
Directory of filters (FilterDir)
  Tracks contents of all filters
  Located at L2 cache shared by all cores
  Given a regular address, gives out the list
  of cores that have it in their local filters
Core
TLB
L1D
SPM
SPMDir
Filter
CPU
Cache directory
Sharers
@
Status
FilterDir
Sharers
@

## Slide 12: Hardware Design
Strided accesses
FilterDir
Local core
Remote core
TLB
L1D
SPM
SPMDir
Filter
TLB
L1D
SPM
SPMDir
Filter

## Slide 13: Hardware Design
Random accesses
FilterDir
Local core
Remote core
TLB
L1D
SPM
SPMDir
Filter
TLB
L1D
SPM
SPMDir
Filter

## Slide 14: Hardware Design
Potentially incoherent accesses
  No mapping in SPMs
  Mapping in local SPM
  Mapping in remote SPM
  No mapping with filter miss
FilterDir
Local core
Remote core
TLB
L1D
SPM
SPMDir
Filter
TLB
L1D
SPM
SPMDir
Filter
HIT
MISS
HIT
MISS
MISS
HIT
HIT
MISS
UP
UP
When data is mapped to some SPM
  Update SPMDir
  Invalidate filters

## Slide 15: Outline
Introduction
  Hybrid memory hierarchy
  Coherence problem
Hardware-software coherence protocol
  Compiler support
  Hardware design
Evaluation
  Experimental framework
  Comparison with cache hierarchies
Conclusions

## Slide 16: Experimental Framework
Gem5
  x86
  64 OoO cores
  L1 32KB , SPM 32KB, L2 256KB
McPAT
  22nm
  Clock gating
NAS benchmarks
  CG, EP, FT, IS, MG, SP
  Tiling transformations by hand
Potentially incoherent accesses
  GCC alias analysis report
  Unused x86 instruction prefix
Parameter | Description
Cores | 64 cores, OoO, 6 instruction wide, 2GHz
Pipeline front end | 13 cycles. 4-way BTB 4K entries, RAS 32 entries. Branch predictor 4K selector, 4K G-share, 4K Bimodal
Execution | ROB 160 entries. IQ 96 entries. LQ/SQ 48/32 entries. 3 INT ALU, 3 FP ALU, 3 LD/ST units. 256/256 INT/FP register file. Full bypass
L1 I-cache | 2 cycles, 32KB, 4-way, pseudoLRU
L1 D-cache | 2 cycles, 32KB, 4-way, pseudoLRU, stride prefetcher
L2 cache | Shared unified NUCA 16MB, sliced 256 KB/core 15 cycles, 16-way, pseudoLRU
Cache coherence | MOESI. Distributed 4-way cache directory 64K entries
NoC | Mesh. Link 1 cycle, router 1 cycle
SPM | 2 cycles, 32KB
DMAC | Command queue 32 entries in-order Bus request queue 512 entries in-order
SPMDir | 32 entries
Filter | 48 entries, fully associative, pseudoLRU
FilterDir | Distributed 4K entries, fully associative, pseudoLRU

## Slide 17: Comparison with Cache Hierarchies
Performance
  Hybrid memory hierarchy (32KB L1 + 32KB SPM)
  Cache hierarchy (64KB L1)
Chart: Speedup
| CG | EP | FT | IS | MG | SP | AVG
 | 1.1274 | 1.032 | 1.1905 | 1.171 | 1.221 | 1.1403 | 0 | 1.147
14%
12%
22%
3%

## Slide 18: Comparison with Cache Hierarchies
Chart: Normalized packets
| CG | EP | FT | IS | MG | SP | AVG
 | 0.764 | 0.99 | 0.711 | 0.804 | 0.717 | 0.664 | 0 | 0.775
23%
20%
34%
2%
NoC traffic
  Hybrid memory hierarchy (32KB L1 + 32KB SPM)
  Cache hierarchy (64KB L1)

## Slide 19: Comparison with Cache Hierarchies
Chart: Normalized energy
| CG | EP | FT | IS | MG | SP | AVG
 | 0.845 | 1.03 | 0.813 | 0.873 | 0.786 | 0.763 | 0 | 0.85167
15%
13%
24%
-3%
Energy consumption
  Hybrid memory hierarchy (32KB L1 + 32KB SPM)
  Cache hierarchy (64KB L1)

## Slide 20: Outline
Introduction
  Hybrid memory hierarchy
  Coherence problem
Hardware-software coherence protocol
  Compiler support
  Hardware design
Evaluation
  Experimental framework
  Comparison with cache hierarchies
Conclusions

## Slide 21: Conclusions
Hybrid memory hierarchy
  Attractive solution for future manycores
  Coherence problem
Hardware-software coherence protocol
  Straightforward compiler support
  Simple hardware design with low overheads
The hybrid memory hierarchy can be programmed with shared memory programming models
The hybrid memory hierarchy outperforms cache hierarchies
  Average speedup of 14%
  Average NoC traffic reduction of 23%
  Average energy consumption reduction of 15%

## Slide 22: Coherence Protocol for Transparent Management of Scratchpad Memories in Shared Memory Manycore Architectures
Thanks for your attention!
Questions?